## Slide 1
Formability with MatFlow:
An open framework for automated formability predictions
lightform.org.uk
Adam Plowman, Patryk Jedrasiak, Sumeet Mishra, Pratheek Shanthraj, João Quinta da Fonseca
LightForm Technical Seminar, October 2020

## Slide 2
Formability
Industry perspective
Rapid growth in use of light alloys in components due to weight-savings and recyclability
Formability must be well-understood to ensure a manufactured components maintain good performance
Our aim: to facilitate this by building infrastructure for generating formability predictions
What do we need to do? Yield functions and forming limits should be quantified

## Slide 3
Our approach
Virtual materials testing
Virtual materials testing and a small set of experimental tests
Simulation not limited to experimentally “easy” deformation modes
Different models exist, e.g.:
  Taylor
  Self-consistent
  Full-field
Full-field models using crystal plasticity most accurate, but expensive
Which method is most fruitful?
Deforming a volume element under different loading regimes using DAMASK (FFT CP)

## Slide 4
Our approach
Computational formability framework
To provide valuable predictions, we must:
  compare results of different models (e.g. is the cheaper model good enough?)
  compare effect of including different experimental data (e.g. is grain morphology important?)
  support heterogeneous data sources/sinks (e.g. different texture data formats; different simulation codes)
We’ve built a framework to make this process straightforward (and worth doing!)
Adopting a pipeline approach means our framework is sufficiently general
Experimental data
Model calibration
Simulate (model A)
Processing
Formability predictions
Simulate (model B)
Formability predictions

## Slide 5
Our approach
Reproducibility and transparency
Our framework has been designed specifically to ensure reproducibility.
Typically:
Outputs:
Publication
Additional outputs:
Generated data (e.g. texture data)
Methods + parameters (e.g. CP parameter optimisation)
Derived data (e.g. fitted yield function parameters)
With our framework:
What is accessible to the materials community?
Data of a virtual materials test
Baker, Monya. ‘1,500 Scientists Lift the Lid on Reproducibility’. Nature News 533, no. 7604 (26 May 2016): 452. https://doi.org/10.1038/533452a.

## Slide 6
MatFlow
The workflow structure: tasks and elements
Task 2: sample orientations
ODF  orientations
Task 3: generate volume element
orientations, model resolution  volume element
do what?
with which method?
with which software?
using Dream.3D
Data of a virtual materials test
Task 4: simulate loading
volume element, load cases, CP parameters  model responses
Task 5: fit yield functions
model responses  anisotropy parameters
Task 1: estimate ODF
EBSD data  ODF
Task 1: get model ODF
modal direction  ODF
Task 1: estimate ODF from CTF file using MTEX
EBSD data  ODF

## Slide 7
MatFlow
Using MatFlow
Profile
Profile file
Machine-agnostic
Task list
Resource options (e.g. num. cores)
Schemas
Software
MatFlow
MatFlow installation on a cluster
MatFlow extensions
matflow-DAMASK
matflow-MTEX
matflow-DefDAP
matflow-formable
matflow go profile
Schemas file
Machine-agnostic
Defines available tasks
Defines commands to run
Links tasks to the extension packages
Software file
Machine-specific
Defines environment to be loaded
Defines software executable names
workflow.hdf5
Auto-archiving
Cloud storage
Public data repositories (via DataLight)
Further analysis
DOI

## Slide 8
MatFlow
Generating formability predictions with MatFlow

## Slide 9
Conclusions
Summary
Developed a framework for generating formability predictions, called MatFlow
Aims to streamline computational work that includes “virtual materials testing”
Workflows are structured to enable comparisons between different methods
Currently writing a paper demonstrating our use of MatFlow in making formability predictions for Surfalex (AA6016A)
Code and demos
MatFlow: github.com/LightForm-group/matflow
MatFlow extension packages: github.com/topics/matflow-software
Demo: MatFlow viewer: matflow.pythonanywhere.com
Demo: running further analysis in Jupyter: mybinder.org/v2/gh/aplowman/matflow-workflows/master
Workflows on Zenodo:
  Yield function fitting: doi.org/10.5281/zenodo.4119131
  Stress-strain curve: doi.org/10.5281/zenodo.4119161